## Sunlumo Media Service October 2015

##### Business/Solar Energy/Environmental Engineering

### Innovative plastic collector now with Solar Keymark certification

#### Suitability of lightweight collector design now certified by external testing institute.

Sunlumo celebrates a further world sensation with its One World Solar Collector: this is the first time that a 100% polymer-based collector from Europe was awarded with Solar Keymark certification. “This certificate stands for reliable quality and safety,” Sunlumo CEO Robert Buchinger declares. Solar Keymark is a quality certificate for solar collectors and solar-thermal systems, that is valid throughout Europe.

Perg, 28 October 2015 – “To be recorded as bearing Solar Keymark certification, the One World Solar Collector had to pass a full test, as specified in the EN12975 standard in force, and to withstand quality assurance in manufacturing.” The pilot series was manufactured by licensee One Sun One World GmbH. Their quality management level meets the requirements of EN ISO 9000: an accredited testing lab takes collector specimens from a production batch. This procedure is only one certification criterion among others. Both the product and the manufacturing process are regularly checked by independent institutions. Every product alteration must be recorded with the institution.

Intelligent product design to reduce material input

Holistic evaluation of the product concept – a completely novel approach – led to the implementation of a new collector model as a result of the industrial design process. Instead of the usual 15 to 20 kilograms per square meter, the plastic-based One World Solar Collector only weighs 8.1 kilograms. In the course of Solar Keymark testing, the polymeric collector was exposed to more than twice the load required by the testing standards for snow, and has yielded excellent results. Even after applying this load, the collector remained undamaged and continued to function properly. Among other things, the tests concerned internal pressure resistance, high temperature resistance, internal and external thermal shock, impact strength, heating performance, over-temperature protection, and pressure resistance. It was the first time that an external testing institute officially confirmed the suitability of this lightweight design for the new collectors.

Turnkey factories for producing polymer-based collectors

Sunlumo issues licenses for the realisation of the innovative One World Solar Collector and also supplies turnkey factories. The factories are available with different levels of automation. Production sites can be customized to clients’ needs, with annual production capacities ranging from 100 to 350 MWth.

Corporate data

Sunlumo Technology GmbH is an international solar company with offices in Austria, China, India and the USA. The company mainly focuses on green technology, solar-thermal engineering, research, development and trade. Sunlumo chiefly targets investors for innovative projects, partners for the development of new technologies in Europe and Asia, as well as dealers in the field of environmental technology. Another key feature of its service range is industrial design for solar energy applications. The managing partners and project managers of Sunlumo, Robert Buchinger and Markus Barek, are also DIN CERTCO-accredited auditors for Solar Keymark certification.

More information at www.sunlumo.at

For any further queries please contact:

Kommhaus

Altausseer Straße 220

8990 Bad Aussee, Austria

T: +43 3622 55344-22

F: +43 3622 55344-17

E: presse@kommhaus.com